## Slide 1: Machine Maintenance Analysis
Group 3
Peter Hara, Adelle Housker, Rami Ibrahimi, Sean Patel, Laith Yousif

## Slide 2: Executive Summary
Group 3 analyzed a synthetic dataset for detecting patterns regarding certain machine failures. Six features and two targets were provided – one target was a binary for failure/no failure, while another was a multivariate variable that included six failure types
Overview
Risks
Null Hypothesis
Approach
One concern about the dataset was that ~97% of the Failure Types were “No Failure”, indicating a very imbalanced dataset; The team addressed this by comparing the accuracy scores from the as-is data versus oversampled and undersampled versions
The team’s initial hypothesis was that the feature “Tool Wear” would have the biggest impact on likelihood of machine failure, but that there would be particular features that would contribute more regularly to each of the six different failure types
Data Overview
Analyses
Conclusions & Next Steps

## Slide 3: 1) Data Overview
  UID: Unique identifier ranging from 1 to 10,000
  ProductID: Consisting of a letter L, M, or H for Low (50% of all products), Medium (30%), or High (20%) as product quality variants and a variant-specific serial number
  Type: Consisting of a letter L, M, or H for Low, Medium, or High
  Air temperature [K]: Generated using a random walk process later normalized to a standard deviation of 2 K around 300 K
  Process temperature [K]: Generated using a random walk process normalized to a standard deviation of 1 K, added to the air temperature plus 10 K
  Rotational speed [rpm]: Calculated from power of 2860 W, overlaid with a normally distributed noise
  Torque [Nm]: Torque values are normally distributed around 40 Nm with an Ïƒ = 10 Nm and no negative values
  Tool wear [min]: The quality variants H/M/L add 5/3/2 minutes of tool wear to the used tool in the process and a 'machine failure' label that indicates whether the machine has failed in this particular data point for any of the indicated failure modes
Synthetic Data
10,000 rows x 10 columns
Source: https://www.kaggle.com/datasets/shivamb/
machine-predictive-maintenance-classification
Features
  Target: 0 (No Failure) or 1 (Failure)
  Failure Type: Heat Dissipation Failure, Overstrain Failure, No Failure, Power Failure, Random Failures, Tool Wear Failure
IDs
Targets

## Slide 4: 2) Analyses
  Dropped ID columns (e.g., UID, ProductID)
  Converted feature "Failure Type" into 5 dummy variables
  Split data into training and test sets
  Scaled data in the feature columns using StandardScaler and MinMaxScaler
  Used one-hot encoding for feature "Type" (e.g., L, M, H)
Data Preprocessor (Scaler, Dummy, OHE)
Data Sampler (Over/Under)
Models
  9 supervised learning regression / classification models
  Grid search to optimize search
  Data Cleaning & Manipulation
  Pipeline

## Slide 5: 2) Analyses – Model Accuracy Scores
Model | As-Is Dataset | Oversampled Data | Undersampled Data
Logistic Regression | 0.79 | 0.79 | 0.79
K-Nearest Neighbors | 0.83 | 0.83 | 0.83
Decision Tree | 0.90 | 0.90 | 0.90
Random Forest | 0.89 | 0.89 | 0.89
Extremely Random Trees | 0.88 | 0.88 | 0.88
Gradient Boosting | 0.88 | 0.88 | 0.88
AdaBoost | 0.87 | 0.87 | 0.87
Support Vector Machine | 0.86 | 0.86 | 0.86
Naïve Bayes | 0.80 | 0.80 | 0.80

## Slide 6: 2) Analyses – Decision Tree

## Slide 7: 2) Analyses – Feature Contribution
Feature | Weight
Torque [Nm] | 0.320955
Rotational speed [rpm] | 0.214712
Air temperature [K] | 0.161565
Tool wear [min] | 0.153936
Process temperature [K] | 0.148831
Feature | P-Values
Torque [Nm] | 1.488773e-102
Rotational speed [rpm] | 2.432644e-83
Tool wear [min] | 1.856158e-26
Air temperature [K] | 1.361908e-19
Process temperature [K] | 3.944958e-11
Component 1 | Weights
Torque [Nm] | -0.996
Rotational speed [rpm] | 0.092
Type = L | -0.008
Type = M | 0.007
Air temperature [K] | 0.003
Feature Importance
Feature P-Values
PCA Analysis
Component 2 | Weights
Type = L | -0.743
Type = M | 0.664
Type = H | 0.079
Torque [Nm] | 0.011
Tool wear [min] | -0.004

## Slide 8: 3) Conclusions & Next Steps
Contrary to our initial null hypothesis, Torque was the leading cause of machine failure according to our regressions
Oversampling vs Undersampling impacted the accuracy scores by ______
Developing an algorithm that only states “No Failure” will be accurate 96.5% of the time and performs better than any of our models or ChatGPT!

## Slide 9: Fin
Reach out to Group 3 with any machine maintenance needs…
Thank you!!